## Slide 1
Team Details
Team name - Cardionyx
Team leader name – Bhavy Tyagi
Problem Statement – Sudden cardiac events can leave a person unable to call for help, and delayed assistance can be life-threatening. Existing wearables lack reliable emergency detection. This project develops a wearable ECG monitor that detects danger and alerts caregivers promptly.

## Slide 2: Brief about the idea
This project presents a wearable cardiac safety monitoring system designed for continuous real-time supervision of individuals at risk of sudden cardiac events. The device uses a chest-mounted ECG sensor to capture the heart’s PQRST waveform and analyzes the electrical activity to identify abnormal rhythms or dangerous patterns. To improve reliability, the system also considers motion and oxygen-level data to distinguish between normal activity and a potential medical emergency.
To enhance detection accuracy, the system integrates an AI-based software layer. ECG waveform data is processed using a deep learning model to identify key abnormalities such as T inversion, ST depression, ST elevation, Pathologic Q wave, Left ventricular hypertrophy, and Poor R progression. These detected features, along with structured ECG and physiological parameters, are evaluated using a machine learning model (XGBoost) to estimate cardiac risk levels.
When an abnormal condition or elevated risk is detected, the user is first alerted through vibration and a phone notification; if there is no response, the system automatically notifies caregivers and emergency contacts with the user’s location and vital information. The objective is not to diagnose a disease but to reduce the delay between a cardiac event and human assistance, providing a continuous safety layer for individuals living alone or at higher cardiac risk.

## Slide 3: Opportunities
Unlike conventional wearables that rely primarily on optical heart rate monitoring, this solution uses real ECG waveform analysis (PQRST) combined with motion and oxygen saturation data for higher reliability. In addition, it integrates an AI-driven software layer that detects clinically significant ECG abnormalities and evaluates cardiac risk using a machine learning model. This combination of hardware-grade sensing and predictive analytics differentiates it from fitness-oriented devices and positions it closer to intelligent cardiac monitoring systems.
Sudden cardiac events become life-threatening mainly due to delayed response. The system continuously monitors ECG signals, verifies abnormalities using multi-sensor validation, and applies AI-based risk assessment to reduce false alarms while improving detection accuracy. When a dangerous pattern or elevated risk is identified, the device alerts the user first and automatically escalates to caregivers with live location sharing if no response is received, thereby minimizing the delay between event onset and assistance.
The unique strength of the solution lies in combining medical-grade ECG monitoring, multi-sensor verification, deep learning–based abnormality detection, and XGBoost-based predictive risk modeling within a wearable emergency response framework. Instead of merely recording health data, the system actively interprets it and converts it into immediate, actionable safety measures.
How different is it from any of the other existing ideas?
How will it be able to solve the problem?
USP of the proposed solution

## Slide 4: List of features offered by the solution
Continuous real-time ECG monitoring using PQRST waveform analysis.
Multi-sensor verification using motion detection and oxygen saturation (SpO₂) data.
Intelligent anomaly detection instead of simple heart-rate threshold alerts.
User warning through vibration and mobile notification before escalation.
Automatic SOS alert to caregivers and emergency contacts if no response is received.
Live location sharing during emergencies.
Event logging and history tracking through the mobile application.
Reduced false alarms through combined physiological and activity analysis.
Designed for daily wearable use and independent living safety.
Low-power operation with wireless Bluetooth connectivity to smartphone.
Multi-level emergency escalation alerts the user first, then caregivers, and if no acknowledgement is received, automatically sends an SOS message (with location and vital status) to nearby hospitals/emergency services.

## Slide 5: Process flow diagram or Use-case diagram

## Slide 6: Wireframes/Mock diagrams of the proposed solution (optional)
Type here

## Slide 7: Architecture diagram of the proposed solution
Type here

## Slide 8: Technologies to be used in the solution
Hardware Technologies – nRF52840 microcontroller with Bluetooth Low Energy (BLE) communication, ADS1292R analog front end for ECG signal acquisition (PQRST waveform), MAX30102 sensor for SpO₂ and pulse monitoring, IMU motion sensor for activity and fall detection, rechargeable Li-Po battery based wearable embedded system.
Embedded & Signal Processing – Real-time ECG signal filtering and PQRST peak detection, anomaly detection algorithms for cardiac irregularities, multi-sensor data fusion (ECG + motion + oxygen level), signal preprocessing and feature extraction pipeline.
Communication & Connectivity – Bluetooth Low Energy (BLE) communication between wearable and smartphone, GPS/location sharing via mobile device, automatic SOS alert messaging system, secure cloud synchronization.
Software & Application – ML model which is trained on 55 different parameters. Mobile application for real-time monitoring and notifications, YOLO-based deep learning model for ECG abnormality detection (T inversion, ST depression, ST elevation, Pathologic Q wave, Left ventricular hypertrophy, Poor R progression), XGBoost-based predictive model for cardiac risk estimation using structured ECG and physiological features, AI-driven risk scoring and decision engine, cloud database/server for storing events and medical data, emergency alert system to notify caregivers and nearby hospital services.

## Slide 9: Usage of AMD Products/Solutions
The wearable device continuously streams physiological data (ECG waveform, motion, and SpO₂) to a mobile application and cloud platform for analysis.
AMD CPU/GPU based systems can be used on the server side to process large volumes of ECG signals and run machine-learning models for detecting abnormal cardiac patterns and improving anomaly detection accuracy.
The system can utilize AMD-powered edge or cloud computing to perform real-time signal filtering, pattern recognition, and predictive health risk analysis.
AMD hardware acceleration can enable faster processing of biomedical data, reducing response time between detection and emergency alert generation.
Future versions of the solution can deploy AI models trained on AMD computing platforms to improve reliability and reduce false alarms

## Slide 10: Estimated implementation cost (optional)
Estimated Implementation Cost (Prototype):
Hardware Components:
nRF52840 BLE microcontroller module – ₹2,500
ADS1292R ECG front-end sensor – ₹1,400
MAX30102 SpO₂ sensor – ₹250
IMU motion sensor – ₹300
Textile ECG electrodes & leads – ₹300
Vibration motor & buzzer – ₹200
Li-Po battery + charging module – ₹400
PCB fabrication & miscellaneous components (resistors, connectors, casing) – ₹1,000
Total Estimated Prototype Cost: ~ ₹6,000 – ₹6,500 per device
In mass production, cost is expected to reduce to ₹2,500–₹3,000 per unit due to bulk PCB manufacturing and integrated modules.
Software and cloud services will be shared infrastructure and not per-device hardware cost.

## Slide 11: Prototype Assets (Optional)
https://github.com/bhav1010/Cardionyx
GitHub Public Repository Link
Demo Video Link (Max: 3 Minutes)